## Slide 1: BLE Hand visualization
By: Shabrya Lott
lotts2@unlv.nevada.edu

## Slide 2: Aim & Accomplishments
Aim
  To measure human hand movements by monitoring and storing accelerometer/gyro data.
Accomplishments
  Learned how to capture data from IMU sensor (6 DOF- MPU 6050)
  Learned how to calibrate and display collected data in a visual manner
  Learned how to make device wireless by using a Bluetooth module (HC-06).

## Slide 3: Schematics

## Slide 4: PCB Layout

## Slide 5: Breadboard

## Slide 6: Design Stages
Components
  ATmega328p – Micro-controller unit
  MPU 6050 – 6 DOF Gyro/Accelerometer
  HC-06 – Bluetooth Module
  Ellipsis- Android Tablet used to Display Sensor data
Interfaces
  Inter-Integrated Circuit communication (I2C): MPU-6050 to Atmega328p
  Universal Asynchronous Receiver/Transmitter (UART) + Bluetooth: Atmega328p to Android device
Visualization
  The data is displayed on Android Application, “Bluetooth Terminal/Graphics”.

## Slide 7: Code Development
Initialization
  Interfaces
    UART - set baud rate, make asynchronous , enable transmitter
    I2C- init TWI clock
  MPU-6050 sensor
    check if device is accessible
    set appropriate registers for a start condition
    find average raw values for calibration
Data Collection
  Read raw values of the X, Y, Z axis of the sensor
  Convert values to actual measurements by subtracting calibration value and dividing by the MSB
Visualization
  Turn data into a printable string
  Special Format for Application: “EValue1, Value2, Value3… \n”
  Changed data type of values for easier visualization on graph

## Slide 8: Video Demonstration
YouTube Video:
https://youtu.be/_NsUO8qaSoY